## Slide 1
Daniel Ferenc,
Physics Department, UC Davis,
and
PhotonLab, Inc.
* Patent Awarded in 2015, Other patent pending
  ABALONE PHOTOSENSOR TECHNOLOGY*
Crucial contributions to our project by
late Eckart Lorenz, MPI Munich and UC Davis, and Tom Ypsilantis, CERN and EP Paris

## Slide 2
In my Keynote lecture:
"The vision of photon counting in the next decade: vacuum and gaseous sensors,“ at the ASPERA Technology Forum, 21-22 October 2010, Munich (https://indico.cern.ch/event/97302/contributions/1288309/)
I predicted that:
- PMTs will become obsolete.
- But HPDs and some similar ideas will prove impractical.
- And promised that the ABALONE technology will be proven.
Today, I am reporting on:
  The proof of concept of the ABALONE photosensor technology
  Unique ABALONE photosensor performance
  The suitability for next-generation astroparticle projects
  The collaboration with Uni-Mainz on the development of new prototypes for IceCube2.

## Slide 6
PMTs – an 80-year Old Manufacture

## Slide 7
ANATOMIC DISPLAY of a PMT (only of its vacuum part)
PHOTOCATHODE ‘FACTORY’
> 180 components
> 400 spot-welds
HAND-MADE

## Slide 8
SMALL GAPD:
 CHEAP
 FAST
10,000 X CONCENTRATION
CRUCIAL:
GLASS ONLY !
NO METALS
NO CERAMICS
NO APDs
NO MCPs
NO ELECTRODES
NO FEEDTHROUGHS

## Slide 9
THE GOAL
OF THE ABALONE PHOTOSENSOR TECHNOLOGY
MASS-PRODUCTION USING THE SAME BASIC TECHNIQUE LIKE THE ONE APPLIED IN THE PRODUCTION OF COMPACT DISCS (CDs)
(Thin-film deposition on dielectric substrates)

## Slide 12
The First IceCube ABALONE “Pre-Prototype”
Collaboration:
UC Davis
Uni-Mainz
PhotonLab, Inc.

## Slide 14
Patent No. 9,064,678

## Slide 15
VACUUM INTEGRITY – A 3.5 YEAR-LONG TEST:
ION FEEDBACK & Time-Of-Flight ANALYSIS
A ~100 X LOWER AFTERPULSING RATE THAN IN THE PMTs
CONSTANTLY IMPROVING, EXCEPT FOR Helium
He is ‘omnipresent,’ so how to understand that difference?

## Slide 16
ABALONE is
Hans Bethe’s Little Playground
(i.e. higher acceleration voltage is better)
-dE/dx ~ 1/b2 ~ m/EK
A. IONIZATION PROBABILITY
Of a ‘vacuum atom’
By a Photoelectron
~ 1/EK
~ 1/HIGH-VOLTAGE

~ 100 X LESS IONIZATION THAN IN A PMT
B. IONIZATION Within
The Photocathode
By an ION
~ 1/EK
~ 1/HIGH-VOLTAGE’

~ 100 X LESS ENERGY DEPOOSITED IN THE PHOTOCATHODE THAN IN A PMT

FEWER AFTERPULSING ELECTRONS GENERATED PER ION IMPACT

LONG-LIVED PC
D. Photoelectron’s energy loss in the Windwlet coating
~ 1/HIGH-VOLTAGE
C. ION IMPLANTATION

## Slide 17
SIGNAL WAVEFORMS –
RAW vs. FILTERED & AMPLIFIED
RAW DATA
FILTERED AND AMPLIFIED DATA
0 10 ns 50 ns 100 ns
LYSO Decay Time ~ 40 ns
20 keV
25 keV
1 secondary photon

## Slide 18
SIGNAL WAVEFORMS - RAW
~ 2 photoelectrons
~ 1 photoelectron
~ 3 photoelectrons
NO FILTERING
NO AMPLIFICATION
5 GHz Scope
U = 25 kV
3X3 SensL J-type GAPD @ -30.5 V
~ Back-Scattered photoelectron
0 50 ns 100 ns

## Slide 19
fwhm = 856 ps
TIMING RESOLUTION
Constant fraction @ 15%
0 1 ns 5 ns
0 0.5ns 2.50 ns 5ns

## Slide 20
SINGLE-PHOTON RESOLUTION
23 keV

## Slide 21
SINGLE-PHOTON RESOLUTION,
DYNAMIC RANGE
AND GAPD-CELL SATURATION

## Slide 22
RE-GAINING LINEARITY –
JUST BY ATTACHING A GAPD WITH SMALLER CELLS TO THE VERY SAME ABALONE PHOTOSENSOR
Monte Carlo

## Slide 23
THE ELECTRON FOCUSING IS ARRANGED
“BEHIND THE (VACUUM) SCENES” (i.e. in the ‘AIR’)
‘AIR’
‘AIR’
CUT AND “EXPORT” THE FIELD LINES TO THE NEIGHBORING UNITS IN A MATRIX
Patent No. 9,064,678 and patent pending PCT/US15/031188

## Slide 24
THE CONCEPT OF ‘TANDEM-ABALONE’ FOR IceCube AND OTHER WATER-CHERENKOV DETECTORS

## Slide 25
Discussions with Sebastian Boeser and Spencer Klein Ice Cube
Patent No. 9,064,678

## Slide 26
Patent No. 9,064,678 and patent pending PCT/US15/031188
A PANEL MAY BE CURVED: CONCAVE OR CONVEX

## Slide 27
Patent No. 9,064,678 and patent pending PCT/US15/031188
MAY BE CURVED: CONCAVE OR CONVEX

## Slide 28
Patent No. 9,064,678 and patent pending PCT/US15/031188
MODULES MAY BE CURVED: CONCAVE

## Slide 29
CONVEX PANELS
HOSTING
ABALONE PIXELS WITH INTEGRATED WINSTON CONES
NO DEAD AREA,
~100% ACCEPTANCE IS POSSIBLE
Like KM3NeT DoM, etc.

## Slide 30
Two ABALONE Prototype Production Facilities
The UC Davis
ABALONE Photosensor Pilot Production Plant (A4P)
Ideal as a demo for the mass-production method or research
But very slow
PhotonLab, Inc.
All the equipment has been gathered
and we are waiting for space
Optimized for quick prototype production
Based on a recent innovation
Expected to be ~20 times faster

## Slide 31
PMT