## Slide 1: Calibration and the Ice Model
Dawn Williams
University of Alabama
IceCube Bootcamp 2021

## Slide 2: IceCube Detector and Ice references
The IceCube Neutrino Observatory: Instrumentation and Online Systems
  https://arxiv.org/abs/1612.05093
Calibration and Characterization of the IceCube Photomultiplier Tube
  https://arxiv.org/abs/1002.2442
The IceCube Data Acquisition System: Signal Capture, Digitization, and Timestamping
  https://arxiv.org/abs/0810.4930
Measurement of South Pole ice transparency with the IceCube LED calibration system
  https://arxiv.org/abs/1301.5361
Evidence of Optical Anisotropy of the South Pole Ice
  https://arxiv.org/pdf/1309.7010.pdf
Photon Propagation through Birefringent Polycrystals
  https://internal-apps.icecube.wisc.edu/reports/details.php?type=report&id=icecube%2F201902001
Energy Reconstruction Methods in the IceCube Neutrino Telescope
  https://arxiv.org/abs/1311.4767
In-situ calibration of the single-photoelectron charge response of the IceCube photomultiplier tubes
  https://arxiv.org/abs/2002.00997

## Slide 3: Acknowledgment
The ice model is developed in the IceCube Calibration working group
Much of the material in this presentation comes from the work of Ryan Bay, Dima Chirkin, Martin Rongen and Chris Wendt and many others

## Slide 4: IceCube
Strings are numbered 1-86
DOMs are numbered 1-60, top to bottom (in ice)
Surface (IceTop) DOMs are numbered 61-64, not used in flasher analysis

## Slide 5: IceCube Strings

## Slide 6: IceCube Digital Optical Module (DOM)
Every DOM in IceCube is equipped with flasher LEDs
This gives us a controlled light source at every location in the detector

## Slide 7: Signal in a Photomultiplier Tube

## Slide 8: DOM Output: single photoelectron
This is what we record when light hits the DOM: a waveform

## Slide 9: Single Photoelectron Charge Distribution
This is measured individually for every single DOM and forms the basis for energy calibration

## Slide 10: DOM output: complex waveform
ATWD
FADC

## Slide 11: Waveforms to pulses

## Slide 12: Pulses in a PMT
Pre-pulses: result of photons striking first dynode instead of photocathode
Late pulses: result of photoelectrons backscattered off the first dynode
Afterpulses: result of ions created near the last dynode that accelerate back to the photocathode and produce multiple photoelectrons

## Slide 13: Pulses in a PMT
Pre-pulses: result of photons striking first dynode instead of photocathode
Late pulses: result of photoelectrodes backscattered off the first dynode
Afterpulses: result of ions created near the last dynode that accelerate back to the photocathode and produce multiple photoelectrons
Time (ns)

## Slide 14: Pulses in a PMT
Pre-pulses: result of photons striking first dynode instead of photocathode
Late pulses: result of photoelectrodes backscattered off the first dynode
Afterpulses: result of ions created near the last dynode that accelerate back to the photocathode and produce multiple photoelectrons

## Slide 15: Noise
Distribution of time between hits for noise events – important for low energy events

## Slide 16: An IceCube neutrino (“Big Bird”)
How do we know how much energy Big Bird has?
How do we know where it comes from?

## Slide 17: The ideal picture
Étienne Bourbeau

## Slide 18: The ideal picture
Étienne Bourbeau

## Slide 19: The ideal picture
Étienne Bourbeau

## Slide 20: The ice model
The ice is as much a part of the detector as the DOMs!
The ice is our calorimeter, support structure and shielding
For a complete history of the ice model see here https://wiki.icecube.wisc.edu/index.php/Ice_models

## Slide 21: Calibration: from photon to data
Propagation through ice
Light source
We need to know how light propagates in ice.
Major propagation processes are absorption and scattering

## Slide 22: Ice vs. water
This type of experiment can be done in water (DUMAND, ANTARES/NEMO/NESTOR  KM3NET, Baikal  GVD) or ice (AMANDA IceCube)
Water has good scattering properties, poor absorption properties
Ice has good absorption properties, poor scattering properties
Scattering affects direction, absorption affects energy
Ice has practical advantages over water for detector construction, IceCube was the first cubic kilometer neutrino detector

## Slide 23: Effect of Scattering in Ice
Light arrives later than it should.

## Slide 24: Effect of scattering in ice (toy simulation of tau double pulse waveform)
No scattering
Scattering

## Slide 25: The ice is complex…
No bubbles in undisturbed ice at IceCube depths (clathrates)
Layers of dust cause depth-dependent scattering and absorption
The dust layers are not horizontal…
And the scattering is anisotropic…
And the melted and refrozen ice in the holes has a bubble column in the center…

## Slide 26: What causes scattering in ice?
Ryan Bay
Multiple dust layers, an especially thick layer at about 2000 m depth is called “THE dust layer” in IceCube vernacular

## Slide 27: Why not Greenland? Ask the IceCube DustLogger
LGM = Last Glacial Maximum, 26.5 kya
MIS4 = Marine Isotope Stage 4, 71 kya
Ryan Bay

## Slide 29: Effects of the dust layer: IC-190331

## Slide 30
Ryan Bay
Absorption in South Pole Ice

## Slide 31: Ice flow in Antarctica

## Slide 32: Dust layer tilt at the Pole
Ryan Bay

## Slide 33: Why not drill deeper? Is shear a problem?
Ryan Bay

## Slide 34: The hole ice
Albrecht Karle

## Slide 36: Anisotropy
What causes the anisotropy in the ice properties?

## Slide 37: Modeling anisotropy
Until recently we thought the anisotropy might be caused by the shape/orientation of the dust grains in ice, but our current thinking is that the anisotropy is caused by birefringence due to the crystal structure of the ice itself.

## Slide 38: Our Understanding of IceCube’s ice
Étienne Bourbeau
Bubble column ??????
“Hole” Ice
Ice
layers
Ice Tilt
RDE’s
anisotropy

## Slide 39: In Reality
Étienne Bourbeau

## Slide 40: In Reality
Étienne Bourbeau

## Slide 41: Sources of light in the ice
The “dust logger” (deployment only)
Occasional glowing due to the DOM HV supply
Dark noise – mostly single hits, mostly in the glass, radioactive decay, scintillation (hundreds of Hz per DOM)
Cosmic ray muons (several kHz)
Products from neutrino interactions
Artificial light sources
  LED flashers
  Laser “standard candle” 💀
  Laser lighting for the “Swedish camera” (R.I.P.)

## Slide 42: Calibration: from photon to data
Propagation through ice
Light source
We use flashers:
To verify that DOMs are properly connected and functioning during commissioning
To verify the detector geometry
To study the optical properties of the ice
To study the response of the DOMs themselves

## Slide 43: Flasher wiki references
https://wiki.icecube.wisc.edu/index.php/Flashers
https://wiki.icecube.wisc.edu/index.php/CDOM_Info

## Slide 44: LED Flasher Board
12 LEDs
Arranged in pairs, evenly spaced 60° apart
1&7, 2&8, 3&9, 4&10, 5&11, 6&12, going clockwise seen from above
1-6 are tilted, upward at about 45° from horizontal
7-12 are horizontal

## Slide 45: Flasher properties
The vast majority of IceCube LEDs are ETG-5UV405-30, nominally 405 nm wavelength, actually 399 nm, FWHM of 14 nm

## Slide 46: cDOMs
8 DOMs each on string 14 and string 79 have multiwavelength flashers called cDOMs
See the CDOM wiki for the appropriate masks
For the remainder of this lesson we will use the standard 400 nm flashers

## Slide 47: Flasher properties: Angular emission profile (beam width)
Nominal beam width is 30° in air
In ice, accounting for refraction from air to glass and glass to ice, the beam width is 10°
Can be modeled as a 2-D Gaussian with σ = 10° in both directions

## Slide 48: Flasher operating parameters
Parameter | Allowed values | Description
string | 1 - 86 | String where flashing DOM is located
DOM | 1 – 60 | Flashing DOM number
brightness | 0 - 127 | LED driver current intensity, up to 240 mA
width | 0 - 127 | 2x duration of LED current pulse, in ns
mask | 0001 - 0FFF | Hex representation of bitmask controlling which LEDs flash
rate | 0 - 610 | Rate of LED flashes in Hz

## Slide 49: Flasher operation: String and DOM
Multiple flashers can be run simultaneously
The data acquisition system can withstand at least 3x the normal background rate from muons (~70 bright flashing DOMs simultaneously)
A typical run might have a few to ~30 flashers simultaneously
Neighboring flashers on the same string cannot run simultaneously
Old DOMs (produced in 2004 and 2005) have “afterburst” properties
Flashers cannot be synchronized using the current firmware

## Slide 50: Running flashers: brightness and width
Maximum photon output per LED is 1.17e10 photons per flash
With all 12 LEDs running this is about equal to a 500 TeV cascade
The brightness and width parameters determine the photon output
  Width: duration of driver current, effectively 10-70 ns
  Brightness: amplitude of driver current, up to 240 mA
Width 15
Width 124

## Slide 51
How light output scales with brightness and width

## Slide 52: Running flashers: mask
LED | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Bit | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
The 12 LEDs can be run in an combination. Each LED is controlled by a bit, and the “mask” is the hex representation of the bits
Example: flash LED 7 only
horizontal
tilted
HEX mask is 0064

## Slide 53: Running flashers: mask
LED | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Bit | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
The 12 LEDs can be run in an combination. Each LED is controlled by a bit, and the “mask” is the hex representation of the bits
Example: flash all tilted LEDs
horizontal
tilted
HEX mask is 003f

## Slide 54: Running flashers: mask
LED | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Bit | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
The 12 LEDs can be run in an combination. Each LED is controlled by a bit, and the “mask” is the hex representation of the bits
Example: flash all horizontal LEDs
horizontal
tilted
HEX mask is 0fc0

## Slide 55: Running flashers: rate
Maximum rate is 610 Hz, lower rates are 610 Hz divided by a power of 2
The setting in the configuration is an integer, the actual value of the rate is the next lowest value to that integer which is 610 divided by a power of 2
So for example if the rate setting is 2, the actual rate is 1.191 Hz = 610 Hz/29

## Slide 56: Flasher data processing
Raw waveform
(ADC counts)
Calibrated waveform
(mV)
Pulses
(PE)

## Slide 57: Flasher data and the ice model

## Slide 58: History of flasher data and the ice model

## Slide 59: The IceCube Upgrade

## Slide 60
IceCube Upgrade sensors are more densely spaced, with multi-PMT designs, increased photocathode area

## Slide 61: Upgrade Calibration Goals
Upgrade timing and geometry measurements
DOM optical efficiency determination in situ to better than 3%
2x reduction in uncertainty due to refrozen hole ice
Determine the source and depth dependence of anisotropy in optical scattering in bulk ice
Measure acoustic properties of bulk ice for Gen2
Measure properties of ice below instrumented IceCube volume
Device | Goal
Cameras | 3
Flashers | 1, 6
POCAM | 2, 3, 6
PencilBeam | 4, 6
Acoustic Modules | 5, 6
Dust Logger | 4, 6

## Slide 62: The future: calibration in the IceCube Upgrade
Device | IceCube | IceCube Upgrade | Note
Flasher LEDs in DOMs | All DOMs | All DOMs | Upgrade spacing will be below a scattering length
Cameras | 1 camera, not onboard DOM | Onboard DOMs, additional standalone cameras | Camera has been very useful in informing us about hole ice conditions
Standalone light sources | 2 laser ”standard candles” | POCAM and Pencil Beam | POCAM and Pencil beam designed to be isotropic/multidirectional and probe hole ice and scattering function respectively
Acoustic sensors | None | Modules on each string | Cross-check geometry measurements, R&D for extended detector calibration
Inclinometers | 50 | All DOMs | Mainboard mounted off the shelf component

## Slide 63: Light sources onboard the modules: LED flashers
mainboard
Calibration board
cameras
flashers

## Slide 64: Cameras
mDOM: 2 outward cameras, 1 downward
D-egg: 3 outward cameras

## Slide 65: External light sources
Pencil Beam
Precision Optical Calibration Module (POCAM)

## Slide 66: The Pencil Beam in the Upgrade

## Slide 67: Summary
The ice is a fundamental part of our detector and knowledge of the ice is critical to the science of IceCube
Our model of the ice has been evolving in complexity ever since IceCube was constructed
The IceCube Upgrade will deliver improved measurements of the ice which will be used as the basis of knowledge for the next generation IceCube detector

## Slide 68: Backup

## Slide 69: Vocabulary
DOM = digital optical module
  Basic sensor unit
String = cable with 60 DOMs
  86 strings in final detector
IceTop = surface detector
InIce = all strings
DeepCore = closely spaced center strings

## Slide 70: Vocabulary
Photomultiplier tube or PMT = light detector
HV = high voltage
Photoelectron: an electron ejected from a metal surface in the PMT by a photon
Mainboard = digitizing electronics
ATWD = analog transient waveform digitizer
  128 samples, 3 ns per sample
FADC = fast analog to digital converter
Waveform = digitized current pulse
Timestamp = time a waveform was recorded
Flashers = onboard LEDs for calibration

## Slide 71: IceCube PMT

## Slide 72: Vocabulary
Hit = single DOM sees light (threshold = 0.25 PE)
Local coincidence = neighboring DOMs see light within a certain time window
Hard Local Coincidence (HLC) = no information is sent on unless local coincidence condition is met
Soft Local Coincidence (SLC) = only minimal information is sent on unless local coincidence condition is met
These decisions are all made in the ice by the onboard electronics

## Slide 73: Vocabulary
Trigger = multiple DOMs hit in a certain pattern or time window
  Simple majority (SMT) = some number of DOMs hit, currently 8, i.e. SMT8
  Calibration trigger = flashers
  Minimum bias/minbias trigger = capture whatever is in the detector regardless of pattern
  Many others

## Slide 74: Vocabulary
Event = all information captured within a certain time window around a trigger
  An event may have multiple triggers
Event Builder = software that constructs events
Processing and filtering (PNF) = software that runs online data reduction
Online = realtime data processing
Offline = non-realtime data processing