## Slide 1
Neutrino and Air Shower Simulations in IceCube
Juan Carlos Díaz-Vélez
IceCube Bootcamp
Madison, WI
June, 2022

## Slide 2: The IceCube Observatory

## Slide 3: Events in icecube
Air shower detection @ surface
Penetrating muon detection in deep ice
Events dominated by cosmic ray muons : 106 µ for every v that interacts in IceCube
Atmospheric v’s
µ
downgoing ν’s
upgoing ν’s
ν

## Slide 4
tree<I3Particle>
(direction, position, energy, type)
OM, vector<MCPE>
OM, vector<MCPulse>
OM, vector<DOMLaunches>
(digitized, PTM waveforms)
I3Particle
(direction, position, energy)
NPEs
OM, vector<DOMLaunches>
(digitized, PTM waveforms)
OM, vector<I3RecoPulse>
Simulation
Reconstruction

## Slide 5
PHOTON PROPAGATION
HitMaker
PPC
CLSIM
HYBRID
Detector
PMT
DomLauncher
TriggerSim
i3SIM
BGND Noise/Muons
Vuvuzela
(noise)
PolyPlopia
(coinc. backgrnd)
PROPAGATION
PROPOSAL
GEANT4
(CLSim)
Generation
CORSIKA
READER
NuGen
MUONGUN
GENIE
Corsika
injector
service
LeptonInjector

## Slide 6: simulaton chain (IT)
Detector
Generation
CORSIKA
TankResponse
Service
PMT
DOM
Trigger
TopSimulator
CORSIKA
Reader
CorsikaKinjector
Service
InIce simulation
PHOTON PROPAGATION

## Slide 7: Generators (cont.)
  Other:
    wimpsim-reader: IceTray interface for WimpSim (FORTRAN stand-alone)

## Slide 8: Generators : CORSIKA (COsmic Ray SImulations for KAscade)
Particles are tracked through the atmosphere until they undergo reactions with the air nuclei or - in the case of instable secondaries - decay.
The hadronic interactions at high energies may be described by several reaction models alternatively:
  VENUS, QGSJET, and DPMJET (Gribov-Regge theory),
  SIBYLL (minijet model).
  neXus, EPOS (combination of QGSJET and VENUS).
  HDPM (Dual Parton Model).
Hadronic interactions at lower energies:
  GHEISHA, FLUKA , or UrQMD models.
For electromagnetic interactions
  Tailored version of EGS4.
  Analytical NKG formulas.
https://web.ikp.kit.edu/corsika/physics_description/corsika_phys.pdf

## Slide 9: Generators : CORSIKA (COsmic Ray SImulations for KAscade)
  weighted events : artificially flat spectrum
    better livetime efficiency @ 10 TeV but poor efficiency @ TeV
    energy-targeted generation of (H,He,CNO,Mg,Fe) with E-1(2)
gamma shower Proton shower Iron shower Muon shower

## Slide 10: DYNSTACK in CORSIKA
Replaces CORSIKA’s post-reaction particle stack with a C++11 plugin
General API for doing things like the neutrino kill threshold, plus helpful extras (take configuration from the steering card, manipulate event headers/trailers, etc)
In mainline CORSIKA since 7.56 (modulo typos)
Write plugins in C++11 without touching corsika.F, depend only on the standard library
Build a better CORSIKA for in-ice background simulation.
Reduce memory and disk requirements for high energy simulations.
Kevin Meagher & Jakob van Santen
Analysis-specific, targeted background simulation

## Slide 11
DYNSTACK in CORSIKA
K. Meagher

## Slide 12
PHOTON PROPAGATION
CLSIM
Detector
PMT
DomLauncher
TriggerSim
i3SIM
BGND Noise/Muons
Vuvuzela
(noise)
PolyPlopia
(coinc. backgrnd)
PROPAGATION
PROPOSAL
Generation
CORSIKA
DYNSTACK
CORSIKA

## Slide 13: MuonGun (IceCube implementation of MUPAGE)
arXiv:0907.5563v1 [astro-ph.IM] 31 Jul 2009

## Slide 14: neutrino-generator
Calculate total path length inside the Earth using injected neutrino geometry.
  Separate the total path length into propagation area (SF) and
  detection volume (FE).
Define a step length dx[m] using propagation area and step number.
For each step:
  Calculate a column depth and Earth's density at the step point.
  Calculate a total cross section at the step point.
  Calculate a probability that the injected neutrino interacts within the step. Try Monte-Carlo, and decide whether an interaction happened within the step.
  If interaction occurred: choose interaction randomly.
    If CC-interaction is selected with injection particle NuMu or NuE, break (event is killed).
    else, generate secondaries and continue to next step.
  If nothing happens, continue next step.
Finish propagation when injected neutrino + secondaries reach surface of detection volume (point F), then process a weighted interaction.
produce a E-γ νµ, νe, ντ with
  PRELIM Earth’s density model
    parton distribution functions
    prop & interaction of neutrinos into a weight

## Slide 15: LeptonInjector/LeptonWeighter
LeptonInjector and LeptonWeighter are designed for large-volume Cherenkov neutrino telescopes such as IceCube.
The neutrino event generator allows for quick and flexible simulation of neutrino events within and around the detector volume
Implements the leading Standard Model neutrino interaction processes relevant for neutrino observatories:
  neutrino-nucleon deep-inelastic scattering
  neutrino-electron annihilation.
This is publicly available code.
https://arxiv.org/abs/2012.10449

## Slide 16: Generators
  Cosmic-ray Air Showers:
    CORSIKA (FORTRAN stand-alone)
    dynstack-corsika (parallel corsika client/server w clsim)
    corsika-reader: IceTray reader for standard format (deprecated)
    CorsikaInjectorService (IceTop)
  Muons:
    MuonGun: parametrization of flux of atm. muons under the ice.
  Neutrinos:
    neutrino-generator: injects neutrinos, propagates them through Earth, forces interaction in detector volume.
    genie-icetray: detailed simulation of neutrino interactions with GENIE. (Used for low-energy simulations)
    LeptonInjector / NuFSGen (not yet available): weighted leptons+weights to account for flux models, interaction models, in-earth propagation, etc.

## Slide 17: Lepton propagation
  PROPOSAL: parametrized interactions with the medium. Comp. Phys. Com. 184, 9 (2013), p2070-2090
    Stochastic energy losses include:
      ionization
      electron-pair production
      bremsstrahlung
      photo-nuclear interaction
      decay
  GEANT4: Detailed particle propagation in media. https://geant4.web.cern.ch/
    3rd-party G4 library used by CLSim to propagate leptons for low-energy simulations (CPU-intensive).
https://doi.org/10.1016/j.cpc.2013.04.001
Notes: Propagator with optimal precision and optimized speed for all leptons

## Slide 18: Photon Propagation
µ energy lost + cascades ➙ photons ➙ p.e.
  Photon propagation : ice properties + PMT response + DOM glass/gel
    Pre-generated lookup splined table :
      I3PhotonicsHitMaker
      Amplitude and time distribution
    Direct photon tracking
      CLSim
      PPC
    Hybrid photon tracking
      HitMaker + CLSim

## Slide 19
Direct photon propagation on GPU
Photon Propagation (PPC, CLSim)

## Slide 20
Photon Propagation (PPC, CLSim)
http://icecube.wisc.edu/~ckopper/muon_with_photons.mov

## Slide 21
polyplopia::PoissonMerger
  Injects background event read from a separate file on top of primary events in the chain by sampling from a Poisson distribution over a time window ∆t.
  Also makes use of a CoincidentEventService that could be drop-in replaced with other event services such as a MuonGun-based service.
  Writes a separate I3MCTree with background particles.
  Writes a combined I3MCPE map for signal and background.
polyplopia::MPHitFilter
  Removes events that don’t produce light in the detector and removes branches of I3MCTrees whose particles don’t produce enough PEs in the detector,
  Reduces the storage requirements.
It is then up to the trigger-sim to split up Q-frames into P-frames events based on triggers.
Coincident atmospheric shower events in IceCube
    Polyplopia
    (from gr., πολύς - polús, “many,”, and ὄψ-ops , "vision")

## Slide 22
http://icecube.wisc.edu/~juancarlos/video/10msec_w_noise.mp4
    Polyplopia
    (from gr., πολύς - polús, “many,”, and ὄψ-ops , "vision")
Coincident atmospheric shower events in IceCube

## Slide 23
—> (MCPEs)

## Slide 25
From distribution of (combined) MCPEs.
Outputs I3MCPulseSeries for each DOM.
MCPEs
DOMLauncher::
PMTResponseSimulator
MCPEs

## Slide 26
MCPEs
MCPEs
MCPE
Weights fromSPE Charge Distribution
http://software.icecube.wisc.edu/documentation/projects/DOMLauncher/index.html
Input: I3MCPEs
Output: I3MCPulses

## Slide 27: PAL pulses
Relative time (ns)
Pre-pulses: photoelectrons ejected from the first dynode,
Late pulses: electrons backscatter from dynode to cathode.
After-pulses: ionization of residual gases by electrons accelerated in the space between dynode.
Relative time (ns)
Chiba University
200
-50
0
10000
2000
8000
6000
150
0
50
100

## Slide 28: DOMLauncher: DOM electronics simulation
Core of detector simulation
  Digitization & timing @ MB
  Hard local coincidence (HLC) triggers
Discriminator
LC-logic
Digitization
Simulated effects
  Electronic noise in the digitizers
  Beacon launches (CPU triggered launches)
  The FPGA Clock phase
  RAPcal time uncertainty

## Slide 29: DOMLauncher: DOM electronics simulation

## Slide 30
Trigger Simulation

## Slide 31
CLSIM
PMT
DomLauncher
TriggerSim
i3SIM
CORSIKA
PROPOSAL
PolyPlopia
Vuvuzela
(noise)
}
CPU
}
GPU
}
CPU
The Shish Kabob
(Computing Resource Optimization)
Optimizing the shish kabob:
  Different parts of the simulation chain have different resource requirements.
    CORSIKA is CPU-intensive and requires little RAM
    Photon propagation run almost exclusively on GPUs
    Detector simulation is CPU bound and requires more memory.
Things to keep in mind:
  Running the whole chain on a GPU node will waste GPU resources and limit your throughput.
  Intermediate storage:
    breaking up chain requires transfering/storing intermediate files.
  Reduce complexity in workflow

## Slide 32: Simprod-Scripts
This project is a collection of scripts, tray segments and IceProd modules used in simulation production. The aim is to provide a central place with standard segments for running simulation in both production and privately.
Tray Segments: IceTray meta-modules that contain several I3Modules with default parameters.
IceProd modules: basic wrappers around tray segments that provide an interface for IceProd.
Scripts: collection of python scripts used in simulation production
Examples: The directory simprod-scripts/resources/examples contains a collection of example scripts for running IPModules
Tests: are run on the build-bots to check that the different parts of the simulation are not broken with each commit to the software repository.
http://software.icecube.wisc.edu/documentation/projects/simprod_scripts/index.html

## Slide 33: Simprod-Scripts
Corsika
MuonGunGenerator
NuGen
GENIE
CLSim
PPC
Detectors
IceTop
http://software.icecube.wisc.edu/documentation/projects/simprod_scripts/index.html
IceProd Modules
$I3_SRC/simprod-scripts/python/modules

## Slide 34: Simprod-Scripts
http://software.icecube.wisc.edu/documentation/projects/simprod_scripts/index.html
        Calibration
        DetectorSim
        GenerateAirShowers
        GenerateCosmicRayMuons
        GenerateFlashers
        GenerateIceTopShowers
Tray Segments
$I3_SRC/simprod-scripts/python/segments
        GenerateIceTopShowers
        GenerateNeutrinos
        GenerateNoiseTriggers
        HybridPhotonicsCLSim
        Polyplopia
        PropagateMuons

## Slide 35: simprod-scripts
$I3_SRC/simprod-scripts/resources/examples/fullSimulation.py
http://software.icecube.wisc.edu/documentation/projects/simprod_scripts/examples/fullSimulation.html
Examples:
./fullSimulation.py -n 10 --seed=43682 --datasetnumber=1 --runnumber=1 --no-hybrid --icemodel=SpiceLea \
            --detector=IC86 --unshadowed-fraction=0.99 --flavor=NuTau --outfile=taus.i3 --skip-calibration \
            --from-energy=1000 --to-energy=10000000 --include-gcd-in-outfile
-n 10 Simulate 10 events (the output file might contain fewer events because not everything will trigger).
--seed=43682 A random number generator seed
--datasetnumber=1 --runnumber=1 A combination of “dataset” and “run” numbers. You can keep the same seed for all of them, each one will give a distinct independent set of events. (So you can think of the combination of seed, dataset and run as the actual random number seed. Or, put another way, there is no need to have different seeds for different runs.)
--no-hybrid Do not use hybrid simulation mode, i.e. propagate everything using direct simulation. There will be no photon tables and things like ice anisotropy/SpiceLea will work.
--icemodel=SpiceLea The other two models are “Spice1” and “SpiceMie”. Including things like WHAM would be trivial if you need it.
--detector=IC86 This will select a GCD file from $I3_PORTS automatically. Currently works for IC86 and IC79.
--unshadowed-fraction=0.99 This is the “DOMEfficiency”, currently named like this for compatibility with other tools that use the same name.
--flavor=NuTau You can set this also to “NuE” and “NuMu”.
--outfile=... The name of your final .i3 file you want to generate.
--from-energy=1000 --to-energy=10000000 The energy range in GeV. Currently not implemented for MuonGun which uses fixed energy ranges. Should be fixed soon.
--include-gcd-in-outfile Use this option if you want to generate output files with GCD frames in them. It makes them much easier to use, but of course wastes some space..

## Slide 36: simprod-scripts
$I3_SRC/simprod-scripts/resources/scripts
(run the individual pieces as broken down by production tasks)
Scripts:
$ python nugen.py -h
            Usage: nugen.py [options]
            Options:
            -h, --help show this help message and exit
            --no-execute boolean condition to execute
            --outputfile=OUTPUTFILE
            Output filename
            --summaryfile=SUMMARYFILE
            XMLSummary filename
            --mjd=MJD MJD for the GCD file
            --seed=RNGSEED RNG seed
            —UseGSLRNG
            …

## Slide 37: simprod-scripts
Exercise: Running scripts:
You can run on cobalt
ssh cobalt
or, preferably, you can run an interactive job on NPX with GPU
ssh submit
The following slides will assume you are on submit (AKA NPX)
commands ending with ‘\’ indicate that the next line is a continuation of the current line

## Slide 38: simprod-scripts
Exercise: Running scripts:
icecube@M16:~$ ssh submitter
[submitter]$
[submitter]$ condor_submit -interactive 'request_gpus=1'
Submitting job(s).
1 job(s) submitted to cluster 120263704.
Waiting for job to start…
Welcome to slot1@gtx-00.icecube.wisc.edu!
[gtx-00]$ cd $_CONDOR_SCRATCH_DIR
[gtx-00]$ cp /cvmfs/icecube.opensciencegrid.org/data/GCD/ \
GeoCalibDetectorStatus_2020.Run134142.Pass2_V0.i3.gz gcdfile.i3.gz
[gtx-00]$ /cvmfs/icecube.opensciencegrid.org/py3-v4.2.0/icetray-env icetray/v1.3.3
************************************************************************
* *
* W E L C O M E to I C E T R A Y *
* *
* Version icetray.stable git:f5d21802 *
* *
* You are welcome to visit our Web site *
* http://icecube.umd.edu *
* *
************************************************************************
[gtx-00]$ python $I3_BUILD/simprod-scripts/resources/scripts/nugen.py \
--outputfile nutau.i3 --nevents 100 \
--seed=123 --procnum 0 --nproc=1 \
--FromEnergy 1e5 --ToEnergy 1e6 --NuFlavor NuTau --UseGSLRNG
[gtx-00]$ dataio-shovel nutau.i3

## Slide 39: simprod-scripts
Exercise: Running scripts:
[gtx-00]$ dataio-shovel nutau.i3

## Slide 40: simprod-scripts
Exercise: Running scripts:
  [gtx-00]$ python $I3_BUILD/simprod-scripts/resources/scripts/clsim.py \
--gcdfile gcdfile.i3.gz \
--inputfilelist nutau.i3 --outputfile mcpes.i3 \
--seed 123 --procnum 0 --nproc 1 --no-RunMPHitFilter \
--UseGPUs --UseGSLRNG
[gtx-00]$ dataio-shovel mcpes.i3
[gtx-00]$ python $I3_BUILD/simprod-scripts/resources/scripts/detector.py \
--gcdfile gcdfile.i3.gz \
--inputfile mcpes.i3 --outputfile det.i3 \
--seed 123 --procnum 0 --nproc 1 --RunID 123 —UseGSLRNG
[gtx-00]$ dataio-shovel det.i3

## Slide 41: simprod-scripts
Exercise: Running scripts:
[gtx-00]$ dataio-shovel mcpes.i3

## Slide 42: simprod-scripts
Exercise: Running scripts:
[gtx-00]$ dataio-shovel det.i3

## Slide 43: simprod-scripts
Exercise: Running scripts:
[gtx-00]$ python $I3_BUILD/simprod-scripts/resources/scripts/corsika.py \
--nshowers 10000 --outputfile corsika_bg.i3 --seed 1234 \
--CORSIKAseed=123 --ranpri 2 \
--corsikaVersion v6960-5comp \
--corsikaName dcorsika --UseGSLRNG \
--skipoptions compress
[gtx-00]$ dataio-shovel corsika_bg.i3
[gtx-00]$ python $I3_BUILD/simprod-scripts/resources/scripts/polyplopia.py \
--gcdfile gcdfile.i3.gz \
--inputfile mcpes.i3 --outputfile merged_pes.i3 \
--seed 1234 \
--backgroundfile corsika_bg.i3 --mctype NuTau \ --UseGSLRNG
[gtx-00]$ python $I3_BUILD/simprod-scripts/resources/scripts/detector.py \
--gcdfile gcdfile.i3.gz \
--inputfile merged_pes.i3 --outputfile det_wcoinc.i3 \
--seed 123 --RunID 123 --UseGSLRNG
[gtx-00]$ dataio-shovel det_wcoinc.i3

## Slide 44: simprod-scripts
Exercise: Running scripts:
[gtx-00]$ dataio-shovel corsika_bg.i3
--inputfile mcpes.i3 --outputfile merged_pes.i3 \
--seed 1234 \
--backgroundfile corsika_bg.i3 --mctype NuTau \ --UseGSLRNG
[gtx-00]$ python $I3_BUILD/simprod-scripts/resources/scripts/detector.py \
--gcdfile gcdfile.i3.gz \
--inputfile merged_pes.i3 --outputfile det_wcoinc.i3 \
--seed 123 --RunID 123 --UseGSLRNG
[gtx-00]$ dataio-shovel det_wcoinc.i3

## Slide 45: simprod-scripts
Exercise: Running scripts:
[gtx-00]$ dataio-shovel merged_pes.i3

## Slide 46: simprod-scripts
Exercise: Running scripts:
[gtx-00]$ dataio-shovel merged_pes.i3

## Slide 47: More on simulation
https://docs.icecube.aq/icetray/main/
http://grid.icecube.wisc.edu/simulation
http://wiki.icecube.wisc.edu/index.php/Simulation_Production
SLACK: #simulation

## Slide 48: flow of experimental and simulation data
data
on-line
off-line
physics analyses
experimental
filter @
South Pole
level 1 filtering
(recreate on-line filter)
level 2 processing
level 3 processing
physics
spade
working groups
P&F computing
core computing
DAQ
working groups
distributed computing
simulation generation
level 3 processing
physics
level 2 processing
level 1 filtering
(recreate on-line filter)

## Slide 49
Simulating the online filter and L2 processing
[gtx-00]$ python filterscripts/resources/scripts/SimulationFiltering.py -h
usage: SimulationFiltering.py [-h] [-i INFILE] [-g GCDFILE] [-o OUTFILE]
[-n NUM] [--qify]
[--MinBiasPrescale MINBIASPRESCALE]
[--photonicsdir PHOTONICSDIR] [--enable-gfu]
[--log-level LOG_LEVEL] [--log-filename LOGFN]
[--needs_wavedeform_spe_corr]
optional arguments:
-h, --help show this help message and exit
-i INFILE, --input INFILE
Input i3 file(s) (use comma separated list for
multiple files)
-g GCDFILE, --gcd GCDFILE
GCD file for input i3 file
-o OUTFILE, --output OUTFILE
Output i3 file
-n NUM, --num NUM Number of frames to process
--qify Apply QConverter, use if file is P frame only
--MinBiasPrescale MINBIASPRESCALE
Set the Min Bias prescale to something other than
default
--photonicsdir PHOTONICSDIR
Directory with photonics tables
--enable-gfu Do not run GFU filter
--log-level LOG_LEVEL
Sets the logging level (ERROR, WARN, INFO, DEBUG,
TRACE)
--log-filename LOGFN If set logging is redirected to the specified file.
--needs_wavedeform_spe_corr
apply_spe_corection in wavedeform.

## Slide 50
Simulating the online filter and L2 processing
[gtx-00]$ python filterscripts/resources/scripts/offlineL2/process.py -h
usage: process.py [-h] [-s] [-i INFILE] [-g GCDFILE] [-o OUTFILE] [-n NUM]
[--dstfile DSTFILE] [--gapsfile GAPSFILE]
[--icetopoutput ICETOPOUTPUT] [--eheoutput EHEOUTPUT]
[--slopoutput SLOPOUTPUT] [--rootoutput ROOTOUTPUT]
[--photonicsdir PHOTONICSDIR] [--log-level LOG_LEVEL]
[--log-filename LOGFN]
optional arguments:
-h, --help show this help message and exit
-s, --simulation Mark as simulation (MC)
-i INFILE, --input INFILE
Input i3 file(s) (use comma separated list for
multiple files)
-g GCDFILE, --gcd GCDFILE
GCD file for input i3 file
-o OUTFILE, --output OUTFILE
Output i3 file
-n NUM, --num NUM Number of frames to process
--dstfile DSTFILE DST root file (should be .root)
--gapsfile GAPSFILE gaps text file (should be .txt)
--icetopoutput ICETOPOUTPUT
Output IceTop file
--eheoutput EHEOUTPUT
Output EHE i3 file
--slopoutput SLOPOUTPUT
Output SLOP file
--rootoutput ROOTOUTPUT
Output root file
--photonicsdir PHOTONICSDIR
Directory with photonics tables
--log-level LOG_LEVEL
Sets the logging level (ERROR, WARN, INFO, DEBUG,
TRACE)
--log-filename LOGFN If set logging is redirected to the specified file.

## Slide 51
Simulation Production
Tokio
You will typically not be generating you own simulation.
Simulating IceCube takes many computing cycles
The collaboration utilizes distributed computing resources from around the world
You can find information on generated datasets in
  http://wiki.icecube.wisc.edu/index.php/Simulation_Production
Simulations are stored in “Data Warehouse”
  In-ince: /data/sim/IceCube/[YEAR]
  IceTop: /data/sim/IceTop/[YEAR]

## Slide 52: IceProd2
Distributed Computing
Data provenance
  Configuration
    which software, what versions,
  when/where it ran, ...
Dataset submission
  Monitor job status, resource usage
  Retry failed jobs - resubmit with different requirements

## Slide 53
Simprod DashBoard
https://grid.icecube.wisc.edu/simulation/DashBoard
Catalog of official MC datasets
Simulation Requests
Dataset and resource Monitoring

## Slide 54
Sim-Prod Requests
Need high statistics simulations?
Discuss with your WG
Submit a request
Priority will be evaluated by tech leads
https://grid.icecube.wisc.edu/simulation/DashBoard/#simreqform

## Slide 55
Weighting
SimWeights:
  https://icecube.wisc.edu/~juancarlos/simulation/Bootcamp_2021_Simulation_Weighting.html
Old IceTray weighting project:
  https://icecube.wisc.edu/~juancarlos/simulation/Bootcamp_2020_Simulation_Weighting.html

## Slide 56: Backup

## Slide 57: Example: High-Energy Sterile Neutrino MC Generation
Spencer N. Axani
Simulating Systematic Uncertainties

## Slide 58
SnowStorm
https://events.icecube.wisc.edu/event/118/contributions/6499/attachments/5362/6082/DiffuseParallel_Brussels_SnowStormMCGlobalfit.pdf
Erik Ganster

## Slide 59: CORSIKA weights
CORSIKA produces events according to the flux given by
The number of events generated is
And the effective livetime of the simulation is given by
where
The rate of events is R = n/T
Weighting
The CORSIKA spectrum is biased with a factor resulting in a flux
And each event is assigned a weight

## Slide 60: neutrino-generator
Calculates the propagation probability (i.e. that the neutrino will reach the detector)
It forces an interaction within a volume around the dector and computes the probability of this interaction
where Pint = TotalInteractionProbabilityWeight, E − γ is the neutrino generation energy spectrum shape, Emin and Emax is the minimum and maximum generation energy of neutrinos, Area is the generation surface, Ω the generation solid angle and T = 1sec is the timescale.
The weight corresponding to a given theoretically motivated neutrino flux is
For more details on how to use OneWeight see:
https://docushare.icecube.wisc.edu/dsweb/Get/Document-44937/OneWeight.pdf