## Slide 1
A free-space optical communications data relay for Antarctica
Marcus Birch1
Francis Bennet1, Tony Travouillon1
Simon Alexander2, John French2
1The Australian National University
2Australian Antarctic Division

## Slide 2: Overview
Telecommunications for Antarctica
Why laser communications could be a solution
What is laser communications
Modelling laser communications for Antarctica
The RINGSS site-testing instrument
Future options for demonstrations

## Slide 3
Telecommunications in Antarctica is hard
Without a fibre connection there is typically a reliance on slow Geostationary internet
Starlink offers a way out (<50Mbps uplink persistently)
Science may yet require higher bandwidth connection for offloading data
This could be done with free-space optical relay ( >10Gbps in bursts)
    Leverage both excellent optical sites (Dome C) to avoid complexity of adaptive optics and the orbital dynamics at the poles

## Slide 4
Leveraging Antarctica/Arctic as a service for satellites
Low-Earth orbit satellites rapidly downlink data in bursts to ground stations around the globe
    e.g. earth observation satellites
Many satellites are bottle-necked by the data rates they can offload
    Reducing data quality/quantity is common
Most Earth-observation satellites are sun-synchronous, making polar locations great for maximizing passes
This has been used effectively by KSAT at SvalSat here and Troll station in Antarctica
Laser communication can provide very high data rate downlinks and take advantage of good optical sites in Antarctica
Can offload effectively from satellites but run into the same relay issues for Antarctica

## Slide 5
Taking the same telecommunications done with fiber optics and propagating over free-space (1.55μm)
Faster than radio with far smaller and lower power terminals on board spacecraft
    200Gbps downlink was demonstrated this year
The narrow beams require direct line-of-sight with very stable pointing
Many similarities with optical astronomy – and struggles with similar issues
    Cloud cover and atmospheric turbulence.
What is free-space optical communication? (FSOC / laser communication)

## Slide 6
FSOC at the Australian National University
We specialize in adaptive optics for astronomical telescopes (VLT, Suburu, Gemini etc.) and operating Siding Spring Observatory
Lots of ongoing work to leverage this expertise into FSOC
Commissioning is about to begin for our new 70cm OGS at Mount Stromlo Observatory
Upcoming project to support a laser link with the crewed Orion capsule on the Artemis II mission in late-24/early 25

## Slide 8
Australasian Optical Ground Station Network
We are working on an extensive Australia/NZ network
Antarctica is the next step

## Slide 9
A basic model:
# of passes x duration of passes x cloud fraction = link durations
Modelling optical ground station performance for the poles
To model OGS performance we assume that links can be made in all conditions when it is clear (ignoring outages due to strong turbulence)
Cloud fraction can be measured from satellites
The number of satellite passes, and their duration requires orbital propagation software.
  Depends on inclination and orbital height
Assume Links are made above 30°
Simple model can reveal complex dynamics if modelling networked OGS with spatio-temporal correlation of cloud fraction (Birch et al. 2023)

## Slide 10
Cloud fraction/Availability
Image credit: John French, AAD
Image credit: John French, AAD
Cloud fraction determines how often an OGS can conduct links
Cloud fraction can be difficult to determine from satellites in the polar regions due to reflectivity of snow and ice
  5 different satellite instruments tested but VIIRS/SNPP handles this issue best among optical
A new suite of meteorology instruments installed at Davis station in 2016 for comparison

## Slide 11
Cloud fraction comparison at Davis Station
Seasonal averages from 2016 show good correlation between VIIRS and cloud camera instrument at Davis station.
Image credit: John French, AAD
Visible all-sky camera uses a simple colour threshold for cloud detection
No data for winter

## Slide 12
Trusting the VIIRS cloud fraction
FSOC is mostly with 1.55μm and able to penetrate cirrus cloud
Further work to refine this with a liquid cloud fraction from CloudSat/CALIPSO
(Listowski et al. 2019, Guyot et al. 2022)

## Slide 14
Orbital Simulations
Polar-orbiting or Sun-Synchronous orbits are common for SmallSats/CubeSats and many existing laser communication terminals are already in these orbits
Sun-synchronous satellite yearly passes
Simulations for different prototypical polar orbiting satellites at example sites
This is the driving reason behind SvalSat/Troll commercial operation

## Slide 15
Modelling this as a function of latitude
Dependent on:
Minimum elevation angle for conducting link
Orbital height
Orbital inclincation
Some satellites will never be seen at the south pole

## Slide 16
Putting it all together to estimate capacity
Picking a bit-rate is mostly arbitrary
200Gbps was demonstrated with a CubeSat this year *
RF is rarely >500Mbps
A single CubeSat terminal could exceed a persistent Starlink capacity by over 10x**
*only in downlink
**with caveats (see above)
Reaching these high bit rates and estimates will depend on turbulence (+ Adaptive optics)
FSOC can offer so much downlink capacity that RF relay will bottleneck any advantage
40TB/day
with current leading-edge technology
at Dome C

## Slide 17
Site-testing with the Ring Image Next Generation Scintillation Sensor (RINGSS)
Turbulence profiling measures the vertical function of turbulence not the integrated seeing (e.g. DIMM)
  Infers coherence time and isoplanatic angle
  Can see boundary layer and free atmosphere
New type of turbulence profiler proposed by Andrei Tokovinin (2021) which is smaller and cheaper than previous methods
  SCIDAR/MASS etc.
Images a defocused ring image from star at high speed to construct azimuthal frequency spectrum and infer profile from prior weighting functions
One is being installed at Siding Spring Observatory
An 8” RINGSS was also installed at NASA JPL Table Mountain Observatory

## Slide 18
RINGSS measures seeing like a DIMM (sector seeing) based on radial motion around the ring while also measuring a profile which can be integrated for the scintillation seeing
Some data from JPL Table Mountain
RINGSS allows us to deploy turbulence profilers cheaply at prospective ground station sites
Mainly targeting low quality sites not typically considered for astronomy
Good agreement with two separate integrated seeing monitors!

## Slide 19
RINGSS on the move
The first profile at Svalbard!
(and maybe the Arctic?)
Demonstrating the capability for size/portability
A more robust MASS/DIMM in a small suitcase

## Slide 20
Pathfinder as a next step
Demonstrate a compact ground station (~30cm) at Antarctica to link with existing polar orbiting FSOC satellite and optical downlink to ground station in Canberra
FSOC still requires time to mature before high-speed uplink is broadly offered and there are more ground stations globally for reliable relay.
High quality sites like Dome C could demonstrate non-AO high bit rate uplink to allow Tbit/week off site (RINGSS could piggyback on mission)
Currently looking at McMurdo, Davis, or Dome C
If you have a spare optical telescope at a base – get in touch!
PIXL-1 is a current DLD CubeSat for downlink-only On-off keying