## Slide 1
Measure the vertical profile of atmospheric turbulence at Dome A with KLTP
Zhaohui Shang
(NAOC)
20250917@Phuket
Collaborators:
Yi Hu (NAOC)
Xu Yang (NAOC)
Ji Ouyang (NAOC)
Bin Ma (SYSU)
Paul Hickson (UBC)
Michael Ashley (UNSW)
CHINARE
15m-AWS
8m-DIMM

## Slide 2: Good seeing is preferred in observations
Atmosphere turbulence causes seeing, which limits the resolution of telescopes;
Seeing at the best mid-latitude sites: ~ 0.6 – 0.8″;
Less turbulent areas: e.g., Dome A, Dome C…
Jupiter
seeing
good
bad

## Slide 3
Three components:
  Free-atmosphere （FA)
  Intermediate
  Boundary-layer
The median FA seeing is 0.31″;
Chance of FA/good seeing:
  31% at 8m (measured)
Best seeing ~0.1″；
Most turbulence from the boundary/surface/ground layer.
Ma et al. 2020
8m
Seeing distribution
Night-time seeing measurements
boundary layer
boundary layer

## Slide 4
DIMM-seeing reflects the smearing effect from the total atmosphere.
Adaptive Optics (AO) needs to know the contribution from different layers/heights.
The need for the vertical turbulence profile (Cn2)
Cn2 is the atmospheric structure constant of refractive index.
seeing
Dome C
Aristidi et al. 2018
Surface/ground layer (SL/GL) dominates the overall seeing at Dome C, Dome A, etc.
Altitude
Cn2

## Slide 5
Instrument: solar/lunar scintillometer
  SHABAR (Beckers 2002)
  Turbulence Profiler (TP) (Hickson & Lanzetta 2004)
  LuSci (Tokovini et al. 2010)
  …
Several sensors record scintillation (turbulence) in ms.
Light paths to S1 and S2 overlap, resulting in correlations between the scintillation recorded by S1 and S2.
Dimensionless measurement, so no calibration is required.
Vertical resolution can be achieved with many baselines.
Using solar/lunar scintillation to measure Cn2
=> Vertical Profile of Cn2
3 sensors (photodiodes)

## Slide 6
Using solar/lunar scintillation to measure Cn2
A 6-channel LuSci at CTIO (Tokovinin et al. 2010)
A SHABAR on the roof of PLATO at Dome A (2009), but it didn’t work.
The Arctic Turbulence Profiler (ATP) at PEARL, Canada (Hickson et al. 2010)

## Slide 7
Our Turbulence Profilers (TP)
Self-contained Turbulence Profiler (STP) – a collaboration with Chilean astronomers.
6 channels, 2 sectors;
Tested in June 2025 @CVO.
E-ELT
VLT
Cerro Ventarrones Observatory (CVO)
NAOC, Beijing

## Slide 8
Our Turbulence Profilers (TP)
KunLun Turbulence Profiler (KLTP)
Following ATP design (Paul Hickson)；
No moving parts
8 channels(layers) for more baselines；
7 sectors covering 252°in Azimuth ;
The Arctic Turbulence Profiler (ATP) at PEARL, Canada (Hickson et al. 2010)
Elevation of Sun and Moon
2025.07-09
Moon
Sun
20°
8

## Slide 9
Our Turbulence Profilers (TP)
KunLun Turbulence Profiler (KLTP)
Tested at NAOC;
Deployed to Dome A in Jan. 2025;
Problems with frosting, etc.
twilight
KLTP raw data
7 sectors
Frosting?
Xinglong Station,
NAOC
Dome A

## Slide 10
Preliminary Results: KLTP
Cn2 from Dome A;
height
Each curve is a Cn2 profile from one dataset of 2 minutes. (total: ~2 hours for each sector)

## Slide 11
Preliminary Results: KLTP
Cn2 from Dome A;
Comparing with Dome C;
same z range
Dome C
Dome A

## Slide 12
Preliminary Results: KLTP
First check: integrating Cn2 to get seeing;
Seems reasonable, but not sure.
5m
10m
20m
Good seeing

## Slide 13
Preliminary Results: KLTP
Integrating Cn2 to get seeing;
Seems reasonable, but not sure.

## Slide 14
Preliminary Results: KLTP
Integrating Cn2 to get seeing;
Seems reasonable, but not sure.
5m
10m
Bad seeing

## Slide 15
Preliminary Results: KLTP, STP
KLTP @Dome A
KLTP @Xinglong,
NAOC
STP @CVO,
Chile
2"
1"
1"
Probably wrong
seeing
Time

## Slide 16
Thanks!
Summary:
KLTP can obtain the turbulence profile at Dome A.
Data analysis needs to be checked and refined.

## Slide 17
Simplified atmospheric layers: ABL+Free atmosphere
credit: Bely 2015
Free atmosphere (FA）
Planetary boundary layer (PBL)
Atmospheric boundary layer (ABL)
Surface/ground layer (GL)
Only 2 layers at Dome A/Dome C…:
  Stable free-atmosphere (FA) on top;
  Near ground turbulence layers: Atmospheric boundary layer（ABL）
Inversion layer