## Slide 1
Observations of Markarian 421 by the upgraded prototype Schwarzschild-Couder Telescope
Luca Riitano
University of Wisconsin-Madison
For the SCT Collaboration and CTAO Consortium
IPA 2026

## Slide 2: pSCT Background
CTAO candidate medium sized telescope
Prototype co-located with VERITAS at Fred Lawrence Whipple Observatory in Arizona
~100 GeV to ~100 TeV energy range
Novel dual-mirror Schwarzschild-Couder design matched with use of silicon photomultipliers (SiPMs)
Undergoing camera upgrade after previous camera detected Crab Nebula in 2020
Notes: More info on reference

## Slide 3: pSCT Background
Full camera will feature 177 modules, 11,328 pixels, and 8-degree FoV
Top sector of camera was populated in April 2026
First light achieved April 2nd with 19 fully functional and substantially upgraded modules
Off-axis observations
  Center of sector is 2.7 degrees off-axis
  Field rotation due to tracking limitations

## Slide 4: Mrk 421 Observations
Simultaneous observing campaign of blazar Markarian 421 in a flaring state with VERITAS and IXPE
Mrk 421 is a nearby (~100 Mpc) blazar and first detected extragalactic TeV source (1992, Whipple)
Observing campaign of 9 nights between April 11th and April 21st (UTC date)
22.5 hours of on-source data and 19.25 hours of matching off-source data
~100min of on-source data used as burn sample
  Burn sample – data to optimize cuts on, excluded from final significance
Obtained VERITAS gamma rays that triggered pSCT for burn sample

## Slide 5: Matched Cosmic Ray
0
175
200
150
p.e.
75
50
25
125
100
VERITAS T4 – (35m from pSCT)
pSCT
Photoelectrons
Notes: Circle is 0.5 degree radius. T4 is 35 meters from psct

## Slide 6: Matched 3.4 TeV Gamma Ray
0
20
40
60
80
100
VERITAS T4 – (35m from pSCT)
pSCT
Photoelectrons

## Slide 7: Matched Gamma Rays

## Slide 8: Data Processing and Quality Cuts
Raw data calibrated and gain corrected
Ctapipe python package used to process charge images
  Applied tailcuts cleaning method
  Extracted Hillas parameters
Quality cuts – removed image if:
  Centroid within 2 pixels of the camera edge or a non-functional module
  Less than 5 pixels passed cleaning

## Slide 9: Hillas Parameters
Method of parameterizing shower images as ellipses using moments
Used in this analysis
  Size/Intensity
  Length
  Width
  Distance
  Alpha
Source
Distance

## Slide 10: Cut Optimization
Burn sample for cut optimization
4 runs/99min of on-source data from April 16th and 19th
Tested various parameters to cut on
Maximized significance of burn sample
Final Cuts:
Intensity > 150p.e.
Length/Intensity < 6e-5 m/p.e.
Width < 0.008m
0.05m < Distance < 0.10m
Alpha < 6 degrees

## Slide 11: Data Quality Plots – Run 400128
Number of Eventsf
Intensity (photoelectrons)

## Slide 12: Data Quality Plots – Run 400128
Intensity (photoelectrons)
Events per Bin

## Slide 13: Data Quality Plots – Run 400128

## Slide 14: Pointing Corrections
Bright star -> waveform baseline voltage variance increase
Identifying stars near Mrk 421 allows for pointing corrections

## Slide 15
Average Mrk 421 Position
VERITAS FoV
Off-axis Observations – FoV Comparison
Full pSCT FoV is 8 degrees
Typical IACT FoV - 3.5 to 5 degrees
Average Mrk 421 offset was ~2.7 degrees from camera center

## Slide 16: Gamma Ray Candidates

## Slide 17: Results of One Night of Observations
Preliminary
Remaining 2.75 hours of data from April 19th used
Elevation matched off- source data used for background
Alpha cut of 6 degrees applied
Significance of 7.8 sigma

## Slide 18: Summary
Observed Mrk 421 in a flaring state shortly after partial camera commissioning
Analyzed night of data taken during good weather with Mrk 421 flaring above Crab flux
19 fully functional modules, off-axis observations, moving source, during camera commissioning, and only one night of data analyzed.
Similar significance to 2020 Crab detection with previous camera but several times less livetime
Detection of a source located 2.5 to 3 degrees off-axis – outside of most IACTs FoV
Outlook
  System improvements over past few months to improve data quality
  Module count to increase to ~70 in the next few months
  Further analysis improvements and analysis of full Mrk 421 campaign to be continued
  Camera expected to be fully instrumented with 177 modules in 2027

## Slide 19: Backup

## Slide 20: pSCT Clock Correction

## Slide 21: Pointing Corrections

## Slide 22: Gamma Ray Candidates

## Slide 23: Cherenkov Telescope Array Observatory (CTAO)
Very high energy (VHE) imaging atmospheric Cherenkov telescope (IACT) array
Three telescope sizes – Large (LST – 23.0m primary), Medium (MST – 11.5m primary), and Small (SST – 4.3m primary)
20 GeV – 300 TeV energy range
La Palma, Spain – 4 LSTs, 9 MSTs
Paranal, Chile – 14 MSTs, 37 SSTs (+ 2 LSTs, +5 SSTs)
Sensitivity from Prod5 – 5th generation of IRFs from 2021
Motivation - exploring relativistic particle accelerators and extreme environments
*Prod5

## Slide 24: Sensitivity
On-axis
3.5º off-axis
*Prod3b

## Slide 25: Angular Resolution
On-axis
3.5º off-axis
*Prod3b

## Slide 26: pSCT Camera

## Slide 27: Upgraded pSCT Camera Module
Module performance paper: https://arxiv.org/abs/2512.12529

## Slide 28: LED Flasher Tests

## Slide 29: Charge Histograms

## Slide 30: Measured Module Performance

## Slide 31: First Camera Sector Testing
First batch of production focal plane modules and front-end electronics modules received in January-February
Optimization, calibration, assembly, and testing of 22 modules / 1408 pixels completed on March 12th

## Slide 32: Minicam Test Setup

## Slide 33: Outlook
Improved simulations of SCTs underway
Camera module behavior thoroughly tested
pSCT camera module fabrication has started
NSF funding for 10 Small-Sized Telescope cameras using similar technology
1,855

## Slide 34: Module Waveform Calibration

## Slide 36: Crab Detection
Crab Nebula detected at 8.6 sigma using data from February 2020
17.6 hours of on and off-source data
Hillas parameterization used to establish gamma-ray selection cuts
Adams et al. (2021)2

## Slide 37: Optics
9.7m primary and 5.4m secondary mirror
48 segments in primary and 24 segments in secondary
On-axis point spread function (PSF) - 2.8’
Excellent off-axis PSF achieved
Field angle (deg)
PSF (arcmin)

## Slide 38: Module Overview
Current module – TARGET7 ASIC
Upgrade module – T5TEA and TARGETC ASICs
SMART ASIC pulse shaper and preamp
Charge (ADC • ns)
Counts
See Ambrosi et al. for SiPM details

## Slide 46: References
Adams et al. Design and performance of the prototype Schwarzschild-Couder telescope camera, J. Astron. Telesc. Instrum. Syst. 8(1), 014007 (2022).
Acharyya et al. The Optical System of the Schwarzschild-Couder Telescope and the Performance Improvement to the CTA, PoS ICRC 2023, 587 (2023).
Cerasole et al. Comparative Study of CTAO Medium-Size Telescope Array Layout Performances in Gamma-Ray Burst Observations. PoS ICRC 2023, 726 (2023).